A+ Guide to IT Technical Support, 9th Edition
Chapter 1
First Look at Computer Parts and Tools
[Speaker Notes: A+ Guide to IT Technical Support, 9th Edition Chapter 1 First Look at Computer Parts and Tools]

---
Objectives
Objectives
- Identify the various parts inside a desktop computer case and describe how they connect together and are compatible
- Identify the various ports, slots, and internal components of a laptop computer and explain special concerns when supporting and maintaining laptops
[Speaker Notes: Objectives Identify the various parts inside a desktop computer case and describe how they connect together and are compatible Identify the various ports, slots, and internal components of a laptop computer and explain special concerns when supporting and maintaining laptops]

---
Objectives
Objectives
- Describe various hardware components in mobile devices and types of wired and wireless connections mobile devices can make
- Describe the purpose of various tools you will need as a computer hardware technician
[Speaker Notes: Objectives Describe various hardware components in mobile devices and types of wired and wireless connections mobile devices can make Describe the purpose of various tools you will need as a computer hardware technician]

---
What’s Inside the Case
What’s Inside the Case
Computer Case
  - Sometimes called “chassis”
  - Holds
    - Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives
    - Tower case – sits upright and can hold several drives
    - Desktop case – lies flat and sometimes holds monitor
    - Mobile case – used with laptops and tablets
    - All-in-one case – used with all-in-one computer
[Speaker Notes: What’s Inside the Case Computer Case Sometimes called “chassis” Holds Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives Tower case – sits upright and can hold several drives Desktop case – lies flat and sometimes holds monitor Mobile case – used with laptops and tablets All-in-one case – used with all-in-one computer]

---
What’s Inside the Case
What’s Inside the Case
Table 1-1 Ports used with desktop and mobile computers
[Speaker Notes: What’s Inside the Case Computer Case Sometimes called “chassis” Holds Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives Tower case – sits upright and can hold several drives Desktop case – lies flat and sometimes holds monitor Mobile case – used with laptops and tablets All-in-one case – used with all-in-one computer]

---
What’s Inside the Case
What’s Inside the Case
Table 1-1 Ports used with desktop and mobile computers (continued)
[Speaker Notes: What’s Inside the Case Computer Case Sometimes called “chassis” Holds Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives Tower case – sits upright and can hold several drives Desktop case – lies flat and sometimes holds monitor Mobile case – used with laptops and tablets All-in-one case – used with all-in-one computer]

---
What’s Inside the Case
What’s Inside the Case
Table 1-1 Ports used with desktop and mobile computers (continued)
[Speaker Notes: What’s Inside the Case Computer Case Sometimes called “chassis” Holds Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives Tower case – sits upright and can hold several drives Desktop case – lies flat and sometimes holds monitor Mobile case – used with laptops and tablets All-in-one case – used with all-in-one computer]

---
What’s Inside the Case
What’s Inside the Case
Figure 1-2 Inside the computer case
[Speaker Notes: What’s Inside the Case Computer Case Sometimes called “chassis” Holds Power supply, motherboard, processor, memory modules, expansion cards, hard drive, optical drive, other drives Tower case – sits upright and can hold several drives Desktop case – lies flat and sometimes holds monitor Mobile case – used with laptops and tablets All-in-one case – used with all-in-one computer]

---
What’s Inside the Case
What’s Inside the Case
Motherboard – sometimes called system board
  - Largest and most important circuit board
- Processor – central processing unit (CPU)
  - Processes most of the data and instructions for the entire system
  - CPUs generate heat and require a heat sink and fan (together called the processor cooler)
    - A heat sink consists of metal fins that draw heat away from a component
[Speaker Notes: What’s Inside the Case Motherboard – sometimes called system board Largest and most important circuit board Processor – central processing unit (CPU) Processes most of the data and instructions for the entire system CPUs generate heat and require a heat sink and fan (together called the processor cooler) A heat sink consists of metal fins that draw heat away from a component]

---
What’s Inside the Case
What’s Inside the Case
Expansion cards - also called adapter cards
  - A circuit board that provides more ports than those provided by the motherboard
  - Today, most ports are provided by motherboards
Figure 1-4 Ports provided by the motherboard
[Speaker Notes: What’s Inside the Case Expansion cards - also called adapter cards A circuit board that provides more ports than those provided by the motherboard Today, most ports are provided by motherboards]

---
What’s Inside the Case
What’s Inside the Case
Memory modules – random access memory (RAM)
  - Temporary storage for data and instructions as they are being processed by the CPU
  - Dual inline memory module (DIMM) slots hold memory modules
Figure 1-6 A DIMM holds RAM and is mounted directly on a motherboard
[Speaker Notes: What’s Inside the Case Memory modules – random access memory (RAM) Temporary storage for data and instructions as they are being processed by the CPU Dual inline memory module (DIMM) slots hold memory modules]

---
What’s Inside the Case
What’s Inside the Case
Hard drives and other drives
  - Hard drives may also be called hard disk drive (HDD)
    - Permanent storage used to hold data and programs
  - Other drives include: optical drive and tape drive
Figure 1-7 Two types of hard drives (larger magnetic drive and smaller solid-state drive) and a DVD drive
[Speaker Notes: What’s Inside the Case Hard drives and other drives Hard drives may also be called hard disk drive (HDD) Permanent storage used to hold data and programs Other drives include: optical drive and tape drive]

---
What’s Inside the Case
What’s Inside the Case
Power supply – also called power supply unit (PSU)
  - Receives and converts house current so that components inside the case can use it
  - Most come with a dual-voltage selector switch
    - Allows switching input voltage from 115V to 220V
[Speaker Notes: What’s Inside the Case Power supply – also called power supply unit (PSU) Receives and converts house current so that components inside the case can use it Most come with a dual-voltage selector switch Allows switching input voltage from 115V to 220V]

---
Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Form factors: standards that describe the size, shape, screw hole positions, and major features of computer cases, power supplies, and motherboards
  - Necessary so that all will be compatible with each other
- Two form factors used by most desktop and tower computer cases and power supplies:
  - ATX
  - Micro-ATX
[Speaker Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards Form factors: standards that describe the size, shape, screw hole positions, and major features of computer cases, power supplies, and motherboards Necessary so that all will be compatible with each other Two form factors used by most desktop and tower computer cases and power supplies: ATX Micro-ATX]

---
Form Factors Used by Computer Cases, Power Supplies, and Motherboards
ATX (Advanced Technology Extended)
  - Most commonly used form factor today
  - Originally developed by Intel in 1995
  - It is an open, nonproprietary industry specification
- An ATX power supply has a variety of power connectors
  - Power connectors have evolved because new technologies require more power
  - Common ATX power connectors are listed on the following slides
[Speaker Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards ATX (Advanced Technology Extended) Most commonly used form factor today Originally developed by Intel in 1995 It is an open, nonproprietary industry specification An ATX power supply has a variety of power connectors Power connectors have evolved because new technologies require more power Common ATX power connectors are listed on the following slides]

---
Form Factors Used by Computer Cases, Power Supplies, and Motherboards
- 20-pin P1 connector: used by the first ATX power supplies and motherboards
- 4-pin and 8-pin auxiliary connectors: used to provide and additional 12 V of power for evolving CPUs
- 24-pin or 20+4-pin P1 connector: the older 20-pin P1 connector still worked in this connector
  - Supported the new PCI Express slots
- 6-pin and 8-pin PCIe connectors: connect directly to the video card
  - Video cards draw the most power in a system
[Speaker Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards 20-pin P1 connector: used by the first ATX power supplies and motherboards 4-pin and 8-pin auxiliary connectors: used to provide and additional 12 V of power for evolving CPUs 24-pin or 20+4-pin P1 connector: the older 20-pin P1 connector still worked in this connector Supported the new PCI Express slots 6-pin and 8-pin PCIe connectors: connect directly to the video card Video cards draw the most power in a system]

---
Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Micro-ATX form factor
  - Major variation of ATX
  - Reduces total cost of a system by:
    - Reducing number of expansion slots on motherboard
    - Reducing power supplied to the board
    - Allowing for a smaller case size
  - Uses a 24-pin P1 connector
    - Not likely to have as many extra wires and connectors as those on the ATX power supply
[Speaker Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards Micro-ATX form factor Major variation of ATX Reduces total cost of a system by: Reducing number of expansion slots on motherboard Reducing power supplied to the board Allowing for a smaller case size Uses a 24-pin P1 connector Not likely to have as many extra wires and connectors as those on the ATX power supply]

---
Form Factors Used by Computer Cases, Power Supplies, and Motherboards
Figure 1-17 This microATX motherboard by Biostar is designed to support an AMD processor
[Speaker Notes: Form Factors Used by Computer Cases, Power Supplies, and Motherboards Micro-ATX form factor Major variation of ATX Reduces total cost of a system by: Reducing number of expansion slots on motherboard Reducing power supplied to the board Allowing for a smaller case size Uses a 24-pin P1 connector Not likely to have as many extra wires and connectors as those on the ATX power supply]

---
Drives, Their Cables, and Connectors
Drives, Their Cables, and Connectors
Hard Drives
  - Two standards:
    - Serial ATA standard (SATA)
      - Used by most drives today
      - Get power from a power cable that connects to the drive using a SATA power connector
    - Parallel ATA (PATA) – slower than SATA
      - Also called IDE interface
      - Used 40-pin ribbon cable and connector
      - Two connectors on a motherboard for two data cables
      - Found in most older desktop computers
[Speaker Notes: Drives, Their Cables, and Connectors Hard Drives Two standards: Serial ATA standard (SATA) Used by most drives today Get power from a power cable that connects to the drive using a SATA power connector Parallel ATA (PATA) – slower than SATA Also called IDE interface Used 40-pin ribbon cable and connector Two connectors on a motherboard for two data cables Found in most older desktop computers]

---
First Look at Laptop Computers
First Look at Laptop Computers
Laptop (notebook): portable computer
  - Variation of a laptop is a netbook
    - Smaller and has less features than laptop
- Comparing laptops to desktop computers
  - Use the same technology as desktops
  - Smaller, portable, and use less power
  - Replacement parts cost more than desktops
- Laptops offer a variety of ports and slots
[Speaker Notes: First Look at Laptop Computers Laptop (notebook): portable computer Variation of a laptop is a netbook Smaller and has less features than laptop Comparing laptops to desktop computers Use the same technology as desktops Smaller, portable, and use less power Replacement parts cost more than desktops Laptops offer a variety of ports and slots]

---
First Look at Laptop Computers
First Look at Laptop Computers
Figure 1-23 Ports and slots on a laptop computer
[Speaker Notes: First Look at Laptop Computers]

---
First Look at Laptop Computers
First Look at Laptop Computers
Ports common to laptops include:
  - USB, FireWire, network, dial-up modem, audio, and video ports
- Most laptops include slots for flash memory cards
- When a laptop is missing a port or slot, you can use a USB dongle to provide the port or slot
  - Examples:
    - USB to RJ-45 dongle to connect to a wired network
    - USB to Wi-Fi dongle to connect to a wireless network
[Speaker Notes: First Look at Laptop Computers Ports common to laptops include: USB, FireWire, network, dial-up modem, audio, and video ports Most laptops include slots for flash memory cards When a laptop is missing a port or slot, you can use a USB dongle to provide the port or slot Examples: USB to RJ-45 dongle to connect to a wired network USB to Wi-Fi dongle to connect to a wireless network]

---
First Look at Laptop Computers
First Look at Laptop Computers
Figure 1-25 USB to RJ-45 dongle provides a network port to connect to a wired network
Figure 1-26 This USB to Wi-Fi adapter plugs into a USB port to connect to a local wireless network
[Speaker Notes: First Look at Laptop Computers]

---
Special Keys, Buttons, and Input Devices on a Laptop
Special Keys, Buttons, and Input Devices on a Laptop
Button or switches might be above the keyboard
  - Most of the same settings that these buttons control may also be changed using Windows tools
  - Some settings might be:
    - Volume
    - Keyboard backlight
    - Touch pad on or off
    - Screen brightness and screen orientation
    - Dual displays
    - Bluetooth or Wi-Fi
    - Media options
    - GPS on or off
[Speaker Notes: Special Keys, Buttons, and Input Devices on a Laptop Button or switches might be above the keyboard Most of the same settings that these buttons control may also be changed using Windows tools Some settings might be: Volume Keyboard backlight Touch pad on or off Screen brightness and screen orientation Dual displays Bluetooth or Wi-Fi Media options GPS on or off]

---
ExpressCard Slots
ExpressCard Slots
- Most peripheral devices on today’s laptops use a USB port to connect to a laptop
- Before USB, laptops offered ExpressCard slots
  - Sometimes called PCMCIA cards
- ExpressCard matches PCI Express and USB 2.0
  - Two sizes: ExpressCard/34 and ExpressCard/54
  - Not backward compatible
  - Hot-pluggable, hot-swappable, and supports autoconfiguration
[Speaker Notes: ExpressCard Slots Most peripheral devices on today’s laptops use a USB port to connect to a laptop Before USB, laptops offered ExpressCard slots Sometimes called PCMCIA cards ExpressCard matches PCI Express and USB 2.0 Two sizes: ExpressCard/34 and ExpressCard/54 Not backward compatible Hot-pluggable, hot-swappable, and supports autoconfiguration]

---
ExpressCard Slots
ExpressCard Slots
Windows services for ExpressCard
  - Socket service establishes communication between the card and the laptop
  - Card service provides the device driver to interface with the card after the socket is created
- Removing card from ExpressCard slot
  - Use the Safely Remove Hardware icon in the notification area to stop one card before inserting another
  - Proceed to eject the card
[Speaker Notes: ExpressCard Slots Windows services for ExpressCard Socket service establishes communication between the card and the laptop Card service provides the device driver to interface with the card after the socket is created Removing card from ExpressCard slot Use the Safely Remove Hardware icon in the notification area to stop one card before inserting another Proceed to eject the card]

---
Docking Stations
Docking Stations
- Some laptops have a connector called a docking port
- A docking station provides ports to allow a laptop to easily connect to a full-sized monitor, keyboard, AC power adapter, and other peripheral devices
- To use a docking station:
  - Plug all peripherals into docking station
  - Connect laptop to the station
  - No software needed
[Speaker Notes: Docking Stations Some laptops have a connector called a docking port A docking station provides ports to allow a laptop to easily connect to a full-sized monitor, keyboard, AC power adapter, and other peripheral devices To use a docking station: Plug all peripherals into docking station Connect laptop to the station No software needed]

---
Laptop Internal Components
Laptop Internal Components
Figure 1-36 Bottom of a laptop with cover removed
[Speaker Notes: Laptop Internal Components]

---
Laptop Internal Components
Laptop Internal Components
List of important components:
  - Battery pack
  - Hard drive
  - CPU, heat sink, and fan
  - Memory
  - Wireless card
  - System board
  - Optical drive
[Speaker Notes: Laptop Internal Components List of important components: Battery pack Hard drive CPU, heat sink, and fan Memory Wireless card System board Optical drive]

---
What’s Inside an All-in-One Computer
What’s Inside an All-in-One Computer
All-in-one computer: uses a mix of components sized for a desktop and a laptop
  - For some components, you’ll need to buy replacements from the manufacturer because they are most likely proprietary
  - See the service manual for specific directions about replacing parts
[Speaker Notes: What’s Inside an All-in-One Computer All-in-one computer: uses a mix of components sized for a desktop and a laptop For some components, you’ll need to buy replacements from the manufacturer because they are most likely proprietary See the service manual for specific directions about replacing parts]

---
What’s Inside an All-in-One Computer
What’s Inside an All-in-One Computer
Figure 1-38 Components inside an all-in-one computer
[Speaker Notes: What’s Inside an All-in-One Computer]

---
Maintaining Laptops and Mobile Devices
Maintaining Laptops and Mobile Devices
General guidelines:
  - Do not touch LCD panel with sharp objects
  - Do not pick up or hold by the lid
  - Use OEM recommended battery packs
  - Do not tightly pack in a suitcase – use carrying case
  - Do not move while hard drive is being accessed
  - Do not put close to appliances generating strong magnetic field
  - Always use passwords to protect your laptop when connected to a public network or if device is stolen
[Speaker Notes: Maintaining Laptops and Mobile Devices General guidelines: Do not touch LCD panel with sharp objects Do not pick up or hold by the lid Use OEM recommended battery packs Do not tightly pack in a suitcase – use carrying case Do not move while hard drive is being accessed Do not put close to appliances generating strong magnetic field Always use passwords to protect your laptop when connected to a public network or if device is stolen]

---
Maintaining Laptops and Mobile Devices
Maintaining Laptops and Mobile Devices
General guidelines (cont’d):
  - Keep notebook at room temperature
  - Keep away from smoke, water, dust
  - Do not power up and down unnecessarily
  - Do not run it while it is in the case, resting on pillow or covered by a blanket
  - Protect notebook against ESD
  - Remove CD/DVD or USB flash drives before traveling
  - Take precautions if notebook gets wet
  - Keep current backups of important data
[Speaker Notes: Maintaining Laptops and Mobile Devices General guidelines (cont’d): Keep notebook at room temperature Keep away from smoke, water, dust Do not power up and down unnecessarily Do not run it while it is in the case, resting on pillow or covered by a blanket Protect notebook against ESD Remove CD/DVD or USB flash drives before traveling Take precautions if notebook gets wet Keep current backups of important data]

---
Maintaining Laptops and Mobile Devices
Maintaining Laptops and Mobile Devices
Cleaning tips:
  - Clean LCD panel with a soft dry cloth
  - Use compressed air
    - To clean keyboard, track ball, and touch pad
    - To blow out air vents
    - Remove keyboard if keys are sticking and then blow air under keys
  - Use contact cleaner
    - Remove battery and clean battery connections
[Speaker Notes: Maintaining Laptops and Mobile Devices Cleaning tips: Clean LCD panel with a soft dry cloth Use compressed air To clean keyboard, track ball, and touch pad To blow out air vents Remove keyboard if keys are sticking and then blow air under keys Use contact cleaner Remove battery and clean battery connections]

---
First Look at Mobile Device Hardware
First Look at Mobile Device Hardware
A smart phone is a cell phone with added capabilities
  - Ability to send/receive text messages with photos, video, or other multimedia content
  - Web browsing
  - Manage email
  - Play games
  - Take photos and video
  - Use a variety of apps
[Speaker Notes: First Look at Mobile Device Hardware A smart phone is a cell phone with added capabilities Ability to send/receive text messages with photos, video, or other multimedia content Web browsing Manage email Play games Take photos and video Use a variety of apps]

---
First Look at Mobile Device Hardware
First Look at Mobile Device Hardware
- Tablet is larger than a smart phone with similar functions
- Most connect to Wi-Fi and Bluetooth and some have cellular network connectivity
  - Some can make phone calls and use MMS
- Phablet – same capabilities of a smart phone or tablet
  - Smaller than a tablet and larger than a smart phone
[Speaker Notes: First Look at Mobile Device Hardware Tablet is larger than a smart phone with similar functions Most connect to Wi-Fi and Bluetooth and some have cellular network connectivity Some can make phone calls and use MMS Phablet – same capabilities of a smart phone or tablet Smaller than a tablet and larger than a smart phone]

---
First Look at Mobile Device Hardware
First Look at Mobile Device Hardware
Other mobile devices
  - E-readers
  - Smart cameras
  - Wearable technology devices
    - Smart watches, wristbands, arm bands, eyeglasses, headsets, and clothing
[Speaker Notes: First Look at Mobile Device Hardware Other mobile devices E-readers Smart cameras Wearable technology devices Smart watches, wristbands, arm bands, eyeglasses, headsets, and clothing]

---
Connection Types
Connection Types
Some ways a mobile device connects to outside world:
  - Wi-Fi local wireless network and cellular network
  - Bluetooth and Infrared
  - Near Field Communication (NFC)
  - Wired connection
  - Tethering and mobile hotspots
[Speaker Notes: Connection Types Some ways a mobile device connects to outside world: Wi-Fi local wireless network and cellular network Bluetooth and Infrared Near Field Communication (NFC) Wired connection Tethering and mobile hotspots]

---
Connection Types
Connection Types
A mobile device can use the following to sense its position:
  - Gyroscope or accelerometer
    - Motion and position sensing device
    - Helps to adjust screen orientation
    - Used by games to sense device movement
  - GPS
    - Mobile devices might contain a GPS receiver
    - Routinely reports its position to the owner of the OS
    - Geotracking: possible for companies to track device’s whereabouts
[Speaker Notes: Connection Types A mobile device can use the following to sense its position: Gyroscope or accelerometer Motion and position sensing device Helps to adjust screen orientation Used by games to sense device movement GPS Mobile devices might contain a GPS receiver Routinely reports its position to the owner of the OS Geotracking: possible for companies to track device’s whereabouts]

---
Storage Devices
Storage Devices
Mobile devices store apps and data on a solid state drive (SSD)
  - A type of flash memory
- A device might have an external slot for a smart card to provide extra storage
Figure 1-49 An Android device might provide a memory card slot to allow for extra storage
[Speaker Notes: Storage Devices Mobile devices store apps and data on a solid state drive (SSD) A type of flash memory A device might have an external slot for a smart card to provide extra storage]

---
Mobile Device Accessories
Mobile Device Accessories
Examples of accessories:
  - Wireless keyboards
  - Speakers
  - Ear buds
  - Headsets
  - Game pads
  - Docking stations
  - Printers
  - USB adapters
  - Credit card readers
[Speaker Notes: Mobile Device Accessories Examples of accessories: Wireless keyboards Speakers Ear buds Headsets Game pads Docking stations Printers USB adapters Credit card readers]

---
Field-Serviceable Parts for Mobile Devices
Field-Serviceable Parts for Mobile Devices
- There are few FRU in mobile devices
- It is possible to replace screens in some mobile devices
  - A support technician is not generally expected to do this
- SIM cards and batteries can be replaced
[Speaker Notes: Field-Serviceable Parts for Mobile Devices There are few FRU in mobile devices It is possible to replace screens in some mobile devices A support technician is not generally expected to do this SIM cards and batteries can be replaced]

---
Tools Used By a Computer Hardware Technician
Tools Used By a Computer Hardware Technician
Essential tools
  - ESD strap (ground bracelet)
  - Flat-head screwdriver
  - Phillips-head or cross-head screwdriver
  - Torx screwdriver set (size T15)
  - Insulated tweezers
  - Extractor
  - OS recovery CD or DVD
- Many other non-essential tools exists
- Use a toolbox
[Speaker Notes: Tools Used By a Computer Hardware Technician Essential tools ESD strap (ground bracelet) Flat-head screwdriver Phillips-head or cross-head screwdriver Torx screwdriver set (size T15) Insulated tweezers Extractor OS recovery CD or DVD Many other non-essential tools exists Use a toolbox]

---
Tools Used By a Computer Hardware Technician
Tools Used By a Computer Hardware Technician
Figure 1-52 Tools used by IT support technicians when maintaining, repairing, or upgrading computers
[Speaker Notes: Tools Used By a Computer Hardware Technician Essential tools ESD strap (ground bracelet) Flat-head screwdriver Phillips-head or cross-head screwdriver Torx screwdriver set (size T15) Insulated tweezers Extractor OS recovery CD or DVD Many other non-essential tools exists Use a toolbox]

---
Post Diagnostic Cards
Post Diagnostic Cards
Post Diagnostic Cards
  - Helps discover, report computer errors and conflicts at power-on self test (POST)
    - Tests performed by startup UEFI/BIOS
Figure 1-56 Post Code Master diagnostic card by Microsystems Developments, Inc. installs in a PCI slot
[Speaker Notes: Post Diagnostic Cards Post Diagnostic Cards Helps discover, report computer errors and conflicts at power-on self test (POST) Tests performed by startup UEFI/BIOS]

---
Post Diagnostic Cards
Post Diagnostic Cards
- Firmware – programs and data stored on the motherboard
- Two types of firmware may be used:
  - BIOS (basic input/output system) contains:
    - System BIOS
    - Startup BIOS
    - BIOS setup
  - UEFI (Unified Extensible Firmware Interface)
    - More robust and secure than BIOS
    - Can assure boot is secure and no rogue OS hijacks the system
[Speaker Notes: Post Diagnostic Cards Firmware – programs and data stored on the motherboard Two types of firmware may be used: BIOS (basic input/output system) contains: System BIOS Startup BIOS BIOS setup UEFI (Unified Extensible Firmware Interface) More robust and secure than BIOS Can assure boot is secure and no rogue OS hijacks the system]

---
Power Supply Tester
Power Supply Tester
Power Supply Tester
  - Measures output of each power supply connector
Figure 1-57 Use a power supply tester to test the output of each power connector on a power supply
[Speaker Notes: Power Supply Tester Power Supply Tester Measures output of each power supply connector]

---
Multimeter
Multimeter
Multimeter
  - Measures several characteristics of electricity in a variety of devices
Figure 1-58 This digital multimeter can be set to measure voltage, resistance, or continuity
[Speaker Notes: Multimeter Multimeter Measures several characteristics of electricity in a variety of devices]

---
Loopback Plugs
Loopback Plugs
Loopback plug
  - Used to test a port in a computer or other device to make sure the port is working
    - May also test the throughput or speed of port
Figure 1-59 A loopback plug testing a network port and network cable
[Speaker Notes: Loopback Plugs Loopback plug Used to test a port in a computer or other device to make sure the port is working May also test the throughput or speed of port]

---
Summary
Summary
- Ports on a computer might include video, RJ-45, audio, S/PDIF, USB, FireWire, eSATA, and PS/2
- Internal computer components include the motherboard, processor, expansion cards, DIMM modules, hard drive, optical drive, tape drive, and power supply
- Form factors used by cases, power supplies, and motherboards are ATX and micro-ATX
- Power connectors include the 20-pin P1, 24-pin P1, 4-pin and 8-pin auxiliary motherboard, 4-pin Molex, 15-pin SATA, 4-pin Berg, and 6/8-pin PCIe
[Speaker Notes: Summary Ports on a computer might include video, RJ-45, audio, S/PDIF, USB, FireWire, eSATA, and PS/2 Internal computer components include the motherboard, processor, expansion cards, DIMM modules, hard drive, optical drive, tape drive, and power supply Form factors used by cases, power supplies, and motherboards are ATX and micro-ATX Power connectors include the 20-pin P1, 24-pin P1, 4-pin and 8-pin auxiliary motherboard, 4-pin Molex, 15-pin SATA, 4-pin Berg, and 6/8-pin PCIe]

---
Summary
Summary
- Most hard drives, optical drives, and tape drives use the serial ATA (SATA) standards
- Laptop computers use function keys to control many features of the laptop
- A laptop may have an ExpressCard/34 or ExpressCard/54 slot for expansion
- Internal laptop components include keyboard, hard drive, memory, smart card reader, optical drive, wireless card, screen, DC jack, battery pack, touch pad, speaker, system board, and CPU, heat sink/fan
[Speaker Notes: Summary Most hard drives, optical drives, and tape drives use the serial ATA (SATA) standards Laptop computers use function keys to control many features of the laptop A laptop may have an ExpressCard/34 or ExpressCard/54 slot for expansion Internal laptop components include keyboard, hard drive, memory, smart card reader, optical drive, wireless card, screen, DC jack, battery pack, touch pad, speaker, system board, and CPU, heat sink/fan]

---
Summary
Summary
- An all-in-one computer uses a combination of components designed for desktop computers and laptops
- Mobile devices an IT support technician may service include smart phones, tablets, phablets, e-readers, smart cameras, GPS devices, and wearable technology devices
- A mobile device might make a connection using a cellular network, Wi-Fi network, Bluetooth, IR, NFC, tethering, creating its own hotspot, or a wired connection
[Speaker Notes: Summary An all-in-one computer uses a combination of components designed for desktop computers and laptops Mobile devices an IT support technician may service include smart phones, tablets, phablets, e-readers, smart cameras, GPS devices, and wearable technology devices A mobile device might make a connection using a cellular network, Wi-Fi network, Bluetooth, IR, NFC, tethering, creating its own hotspot, or a wired connection]

---
Summary
Summary
- Common tools for a computer hardware technician include an ESD strap, screwdrivers, tweezers, flashlight, compressed air, and cleaning solutions and pads
- Special tools a PC support technician might need include a POST diagnostic card, power supply tester, multimeter, and loopback plugs
[Speaker Notes: Summary Common tools for a computer hardware technician include an ESD strap, screwdrivers, tweezers, flashlight, compressed air, and cleaning solutions and pads Special tools a PC support technician might need include a POST diagnostic card, power supply tester, multimeter, and loopback plugs]